## Slide 1
SIMONE Forecast System
ML-Based Gas Consumption Forecasting
SIMONE Research Group · 2026

## Slide 2
The Challenge
• Gas TSOs need accurate demand forecasts for operational planning
• Traditional methods rely on manual estimation or simple extrapolation
• Weather sensitivity, seasonal patterns, and node-specific behavior are hard to capture
• Errors in forecast → inefficient compression, linepack issues, supply imbalances

## Slide 3
Our Solution
• Machine learning model trained on historical SIMONE reconstruction scenarios
• Automatic weather integration (5 temperatures per country)
• Per-node prediction with automatic correction from yesterday’s actuals
• Fully integrated with SIMONE — reads data and writes forecast scenarios

## Slide 4
Architecture Overview
Core Scripts
• train.py — model training pipeline
• forecast.py — prediction generation & SIMONE integration
Data Flow
• SIMONE scenarios → Parquet → ML model → Forecast CSV → SIMONE scenario
Weather
• Open-Meteo API (free, no API key needed)
Storage
• SQLite for metadata, weather cache, extraction tracking

## Slide 5
Training Pipeline
1. Extract reconstruction scenarios from SIMONE (parallel processing)
2. Download historical weather for 5 representative cities
3. Feature engineering (time, weather, node statistics, customer attributes)
4. Train multiple ML models (LightGBM, XGBoost, Random Forest, Gradient Boosting)
5. Auto-select best model by validation RMSE

## Slide 6
Feature Engineering
Time Features
• Hour, day of week, month (+ sin/cos cyclic encoding)
Weather
• 5 regional temperatures, wind speed, humidity, feels-like
Node Identity
• Encoded node ID, mean consumption, hourly profile shape
Customer Attributes
• Optional type/category from SIMONE user attributes
Calendar
• Holiday and weekend flags

## Slide 7
Weather Integration
• Open-Meteo API: free, global coverage, hourly resolution
• Country selector: auto-picks 5 largest cities per country
• 5 temperatures allow model to learn regional weather sensitivity
• Manual CSV import as fallback (when API unavailable)
• Historical + 48-hour forecast weather supported

## Slide 8
Model Training Results
• Multi-method comparison: LightGBM vs XGBoost vs Random Forest vs Gradient Boosting
• Automatic best model selection (lowest RMSE on validation set)
• Feature importance analysis reveals key consumption drivers
• Typical accuracy: RMSE within 5–15% of mean consumption (network dependent)

## Slide 9
Forecast Generation
• Reads trained model + latest weather forecast
• Generates per-node hourly predictions
• Per-node correction: compares yesterday’s prediction vs actual → adjustment factor
• Resampling to any interval (15 min, 30 min, 60 min)
• Writes forecast scenario (FORECAST.RDF) directly to SIMONE

## Slide 10
Per-Node Correction
• Yesterday’s reconstruction scenario provides actual consumption
• Model predicts yesterday with same weather conditions
• Ratio actual / predicted = correction factor per node
• Dampened: factor clamped to [0.5, 2.0], blended 50/50 with 1.0
• Result: forecast adapts daily to real network behavior

## Slide 11
SIMONE Integration
• Reads scenarios via SIMONE API (simone_read, simone_varid_array_python)
• Writes forecast via simone_write_array
• Automatic unit conversion (training unit → current network default)
• Network / scenario auto-detection from open SIMONE session
• Compressor station fuel nodes automatically excluded

## Slide 12
Multi-Language Support
• 16 languages: EN, CZ, DE, PL, HU, FR, IT, ES, HR, RU, SK, UA, PT, JP, CN
• Auto-detection from SIMONE installation language
• All GUI dialogs, log messages, and country names translated
• GUI via PowerShell WinForms (no additional dependencies)

## Slide 13
Deployment Options
Interactive Mode
• GUI dialogs launched from SIMONE menu
Batch Mode
• --batch flag, reads configuration from FORECAST.INI
Extract-Only Mode
• Daily incremental data extraction for continuous improvement
Packaging
• Pre-built Python wheels, no pip needed
• No external dependencies beyond SIMONE Python SDK

## Slide 14
Key Benefits
• Automated — no manual forecast estimation needed
• Accurate — ML captures weather sensitivity + node-specific patterns
• Adaptive — daily correction from actual data
• Integrated — reads / writes SIMONE scenarios natively
• Scalable — parallel extraction, works with any network size
• Multilingual — 16 languages, auto-detected from SIMONE

## Slide 15
Summary & Next Steps
• Production-ready forecasting integrated into SIMONE
• Continuous improvement: more data → better model
• Daily workflow: extract today → forecast tomorrow
• Future: real-time integration, ensemble models, pressure forecasting