## Slide 1
Requirements Workshop
Gas Dispatch System — Bapco Upstream
June 2026 | Video Call
Bapco Upstream · Bilfinger BTME · SIMONE Research Group

## Slide 2
Agenda
1. System overview — what we're building (10 min)
2. High-level decisions — fluid types, network, timeline (30 min)
3. Module walkthrough — need it or not? (45 min)
4. Open questions per department (20 min)
5. Next steps and homework (10 min)
Note: We have prepared a Requirements Register (397 items).
We will NOT go through it line by line today.
Instead, we decide per module. The register will be sent for
offline review — you mark Yes / No / TBD per requirement.

## Slide 3
What We're Building
Dispatching Solution = Modeling + Analysis + Decision Support
The system READS from SCADA — it NEVER controls without operator approval.
Independent from SIS / ESD / pressure protection.
Network: Gas Distribution Network (GDN) — domestic gas (EOG) + RLNG
Core modules:
Simulation Engine — real-time hydraulic/thermal model of the gas network
State Estimation — corrects SCADA data, fills gaps, calculates line pack
Leak Detection (CPM) — continuous monitoring, alarm, location, rate
Look-Ahead Prediction — what happens in next 1–72 hours
Scenario / What-If — capacity analysis, isolation, survival time
Operator Training Simulator — same model, instructor + trainee
Confirmed from Business Rules (no longer optional):
Dispatch Scheduling · Nominations · Curtailment · Quality Tracking
LNG Cargo Scheduling · Customer Reconciliation · Billing Inputs
Still to be decided:
Pig Tracking · Compressor Optimization

## Slide 4
Reference Architecture
[ Architecture diagram will be shown on screen — see architecture_diagram.png ]
7 layers:
1. External Systems — SCADA, Historian, GIS, ERP, Weather, LNG, GC
2. Integration / DMZ — firewall-protected interfaces
3a. Online Engines — simulation, state estimation, leak detection, prediction
3b. Offline / Interactive — scenarios, OTS
4. Model & Config — network editor, calibration, optimization
5. Reporting & Visualization — displays, trends, dashboards, export
6. Data Layer — real-time DB, archive (5+ years), audit trail
7. Hardware — primary/standby servers, workstations, UPS
On-premises deployment. Primary + Hot Standby. Auto-failover < 5 min.
35% spare capacity on all servers. Dual power supply. NTP synced.

## Slide 5
Decisions Needed Today
These shape the entire specification
Already answered from Business Rules Document:
✓ Gas network (domestic EOG + RLNG)
✓ Multiple supply sources with priority order
✓ Nominations, curtailment, scheduling — all required
✓ LNG terminal integration required
✓ Customer portal (cloud-based nominations)
✓ 4-tier curtailment priority + allocation hierarchy
Still need answers today:
1. Network size — how many pipelines, stations, km? Pressure range?
2. Compressors in the network? How many?
3. How many control rooms? 24/7 shifts?
4. SCADA vendor and version? Interface protocol?
5. Historian? GIS? ERP system?
6. Existing dispatching/monitoring systems to replace?
7. Target go-live date? Hard deadlines?
8. Hardware — Contractor or Bapco supply?
9. Warranty preference — 12 or 24 months?
10. Pigging operations — performed? Tracking needed?

## Slide 6
Module Walkthrough — Core Modules
For each: Do you need this? Any specific requirements?
Simulation Engine
Real-time hydraulic model of your network. Required for everything else.
→ Expected answer: YES (mandatory foundation)
State Estimation
Corrects SCADA data, detects bad sensors, calculates line pack.
→ Expected answer: YES
Leak Detection (CPM)
Continuous monitoring. Alarm + location + rate.
Q: Which pipeline segments to monitor? Sensitivity targets?
Look-Ahead Prediction
Predicts next 1–72 hours. Early warnings for pressure/capacity issues.
Q: What prediction horizon do you need? What triggers interest you?
Scenario Management / What-If
Capacity analysis, isolation analysis, survival time.
Q: Who needs access — dispatchers only, or also planners/engineers?
Operator Training Simulator (OTS)
Same model, instructor + trainee stations.
Q: How many trainees? What emergency scenarios to practice?

## Slide 7
Module Walkthrough — Optional Modules
Need it? Yes / No / Maybe later
CONFIRMED (from Business Rules — no longer optional):
✓ Dispatch Schedule Generation
EOG for base load, RLNG for peaks, storage/line-pack when needed
✓ Customer Nominations & Reconciliation
Day-ahead, hourly (major), intra-day re-nom, freeze period, imbalance
✓ Gas Quality Tracking
Two sources (EOG + RLNG) with different compositions
✓ LNG Cargo Scheduling
Cargo ETA, regas capacity, terminal maintenance windows
✓ Curtailment Management (4-level)
Tiered allocation + load shedding + emergency response
✓ Billing / Contractual (take-or-pay, imbalance penalties)
STILL TO BE DECIDED:
? Pig Tracking — do you perform pigging?
? Compressor Optimization — are there compressors in the GDN?
? Demand Forecasting — beyond what prediction engine provides?

## Slide 8
Interfaces — What Connects to What?
Confirmed interfaces:
✓ SCADA → Dispatching Solution (primary data source)
✓ Dispatching Solution → SCADA displays (read-only results)
✓ LNG Terminal — send-out, cargo scheduling, regas, composition
✓ Customer Nomination Portal (cloud-based)
✓ Gas Chromatographs (via SCADA) — composition data
Likely interfaces:
Historian (for offline analysis, historical events)
GIS (for pipeline geographic data)
To be confirmed:
ERP — nomination data, billing inputs, reconciliation?
Weather data — available source in Bahrain?
Questions:
• SCADA vendor and version? Interface protocol?
• Historian — OSIsoft PI? Honeywell PHD? Other?
• GIS — ArcGIS? QGIS? Other?
• ERP — SAP? Oracle? What data exchange?
• LNG terminal system vendor?
• Customer portal — existing or new?

## Slide 9
Cybersecurity & Safety
Safety:
• System is completely independent from SIS / ESD / pressure protection
• If Dispatching Solution fails — SCADA and all safety systems unaffected
• System NEVER issues control commands
Cybersecurity:
• IEC 62443 compliance — dedicated network zone, firewall, DMZ
• Role-based access control, individual accounts, MFA for remote
• Full audit trail — all logins, changes, alarm actions logged
• On-premises deployment (no cloud for real-time)
Questions:
• What is Bapco's IEC 62443 Security Level target?
• Bapco IT/OT security policies we should align with?
• Approved antivirus / endpoint protection solution?
• SIEM system for log export? Format (syslog, CEF)?
• Restrictions on software country of origin?

## Slide 10
Training & Operations
9 training courses prepared:
TRN-001 System Overview (all stakeholders, 0.5 day)
TRN-002 Operator Basic (dispatchers, 3 days)
TRN-003 Operator Advanced (senior ops, 2 days)
TRN-004 Leak Detection Operations (2 days)
TRN-005 Scenario Management & Planning (2 days)
TRN-006 Network Model Maintenance (3 days)
TRN-007 System Administration (IT/OT staff, 3 days)
TRN-008 OTS Instructor Training (2 days)
TRN-009 Train-the-Trainer (2 days)
Questions:
• How many operators to be trained?
• How many shift groups (repeat sessions needed)?
• Training location — on-site only, or also at vendor premises?
• Interest in training-in-residence during implementation?
• Specific emergency/curtailment scenarios for OTS?
• Arabic language needed for UI or documentation?

## Slide 11
Testing & Acceptance Path
FAT — Factory Acceptance Test (at vendor premises)
All functionality demonstrated with simulated data
iFAT — Integrated FAT (at vendor premises)
End-to-end test with replayed SCADA data
SAT — Site Acceptance Test (at Bapco site)
Live SCADA data, all interfaces, real conditions
Performance & Accuracy Testing
Model accuracy verification, leak detection sensitivity analysis
Provisional Operation Period (POP)
30–60 days continuous unattended operation
Clock resets on any unplanned downtime > 12 hours
Final acceptance conditional on POP completion
Question:
• POP duration preference — 30 or 60 consecutive days?
• Bapco witnesses at FAT — how many people, travel to where?

## Slide 12
Project Timeline
Week 1 (19 May) — Kick-off
✓ Completed
Week 2–3 (June) — Workshops
← WE ARE HERE
Requirements confirmed, Excel register completed by departments
Week 3 (9 June) — First Specification for Review
Complete draft issued to Bapco + Bilfinger for comments
Weeks 4–5 — Review & Finalization
Incorporate comments, resolve open items
Final tender-ready specification package delivered
Implementation (indicative, after tender award):
Months 1–2: Detailed design
Months 3–6: Model construction + FAT
Months 7–10: Installation + SAT
Months 10–12: Tuning + Training
Months 12–15: POP + Final acceptance

## Slide 13
Next Steps & Homework
After this workshop, we will send you:
1. Requirements Register (Excel, 397 items)
→ Fill in column G: Applicable? Yes / No / TBD
→ Add notes in column H where needed
→ Yellow items specifically need your input
→ Deadline: [TBD] days after this workshop
2. Architecture diagram (PNG/PDF)
→ For your internal review and distribution
3. Draft specification package (17 documents)
→ For reference — full details behind each requirement
We need from you:
• Pipeline network topology data (P&IDs, alignment sheets)
• SCADA point list (or representative sample)
• GIS data (if available)
• Historical SCADA data for model calibration
• Bapco IT/OT security policies
• Completed Requirements Register

## Slide 14
Questions?
Thank you